## Slide 1: Enhanced Photometric Stereo with Multispectral Images
Tsuyoshi Takatani† Yasuyuki Matsushita‡ Stephen Lin‡
Yasuhiro Mukaigawa† Yasushi Yagi†
† Osaka University ‡ Microsoft Research Asia
[11 – 4] International Conference on Machine Vision Applications 2013

## Slide 2: Introduction
Photometric stereo
  Based on Lambert’s cosine law
Observed intensity
Albedo
Normal vector
Light direction
Camera
Normal map
Light
Light
Light

## Slide 3: Question
How to get the intensity?
Color
Gray
Normal map
Error map
2.56 (2.63)
Avg. angular error (var.)
Red
Green
Blue
1.42 (1.02)
5.37 (11.42)
13.43 (44.13)
Accuracy varies with wavelength
Red plastic
from MERL BRDF
Gnd. truth

## Slide 4: Purpose
Improve the accuracy of photometric stereo using multispectral information
  Lambertian photometric stereo
Wavelength 1
Wavelength 2
Wavelength 3
Photometric stereo
with different wavelengths
Merge

## Slide 5: Causes why accuracy varies with wavelength
Noise
  Signal to noise ratio (SNR) changes w.r.t. a surface color
Subsurface scattering
  Degree of penetration changes w.r.t. wavelength of the light
Red object
R channel
B channel
Low SNR
Red light
Blue light

## Slide 6: How to obtain a better result
The effect of noise and subsurface scattering
Obtain a better result
  Small effect of noise and subsurface scattering
   More consistent with Lambert model
Noise
Subsurface scattering
Observation: Not consistent with Lambert model
How close the observation is to Lambert model

## Slide 7: Key idea: Check of consistency with Lambert model
Rank of observation matrix
 | Perfect Lambert model | With noise and subsurface scattering
1 | 59.81 % | 67.47 %
2 | 21.86 % | 16.26 %
3 | 18.30 % | 4.59 %
4 | 0.01 % | 3.32 %
5 | 0.01 % | 1.38 %
Total | 99.99 % | 93.02 %
Rank of observation matrix
 Key of consistency with Lambert model
  Contribution ratio of the eigenvalues by PCA

## Slide 8: Identification of optimal wavelength
Evaluation based on matrix rank analysis
Flow
Optimal wavelength when is minimum
Wavelength 1
Wavelength 2
Wavelength 3
 | Wavelength 1 | Wavelength 2 | Wavelength 3
 | 0.960 | 0.985 | 0.642
 | Wavelength 1 | Wavelength 2 | Wavelength 3
 | 0.960 | 0.985 | 0.642
(: -th eigenvalue of )
 | Wavelength 1 | Wavelength 2 | Wavelength 3
 | 0.840 | 0.831 | 0.855
 | Wavelength 1 | Wavelength 2 | Wavelength 3
 | 0.840 | 0.831 | 0.855
 | Wavelength 1 | Wavelength 2 | Wavelength 3
 | 0.687 | 0.852 | 0.968
 | Wavelength 1 | Wavelength 2 | Wavelength 3
 | 0.687 | 0.852 | 0.968
Observe
Segmentation
Compute a normal map at each wavelength
Merge normal maps
at optimal wavelengths

## Slide 9: Experiment on simulation images
Rendered forty images of an egg-shaped object
  MERL BRDF: Blue-acrylic, Green-plastic, Light-brown-fabric, Orange-paint, Purple-paint, Red-phenolic, Yellow-matte-plastic
Rendered image
Ground truth
Segmentation
Optimal wavelengths
Red channel
Green channel
Blue channel
Grayscale
Ours
Normal map
Angular error
(Avg. / Var. [deg])
5.88 / 0.73
4.16 / 0.49
10.40 / 1.51
4.29 / 0.37
3.14 / 0.16

## Slide 10: Discussion for experiment on simulation images
The effect of noise
The effect except SNR
Red channel
Grayscale
Ours
4.29 / 0.37
3.14 / 0.16
In some regions, the result by each channel images has less error
R
G
B
Optimal wavelength
Orange-paint region
Brightness
Channel | Angular error | Evaluation value
Red | 2.17 | 0.767
Green | 3.03 | 0.812
Blue | 12.02 | 0.897

## Slide 11: Experiment on real images
Setup
  Nine wavelengths (450, 488, 580, 650, 694, 730, 780, 880, 940[nm)
  Recorded under 12 different lighting directions
  Target: Plushie
    made of fabric of different colors
Camera
Translation stage
to change the filters

## Slide 12: Result by our method
Segmentation (9 segments)
Target object (plushie)
Optimal wavelengths
Grayscale
Ours
Removed texture

## Slide 13: Results by different wavelengths
450nm
488nm
580nm
650nm
694nm
730nm
780nm
880nm
940nm
Grayscale
Ours

## Slide 14: Conclusion
Enhanced Lambertian photometric stereo with multispectral images
Experiments on simulation and real images
  Better than using grayscale images
  Available even with RGB images
[Future work]
  Extend for other parametric reflectance models
  Estimate the ideal rank of observation matrix
    Ideal rank from grayscale images
  Improve the way to identify the optimal wavelength
    Chose one observation  Remove bad observations
Grayscale
Ours

## Slide 15: Thank you for your listening
Optimal wavelength
when is minimum
Wavelength 1
Wavelength 2
Wavelength 3
Observe
Segmentation
Compute a normal map at each wavelength
Merge normal maps
at optimal wavelengths
Grayscale
Ours
4.29 / 0.37
3.14 / 0.16
Grayscale
Ours
Experiment on simulation images
Experiment on real images

## Slide 16: Light source
Halogen bulb
Chart: Wavelength [nm]
| 334 | 340 | 365 | 394 | 415 | 436 | 450 | 467 | 488 | 510 | 532 | 550 | 580 | 610 | 636 | 650 | 676 | 694 | 730 | 766 | 780 | 800 | 830 | 852 | 880 | 905 | 940
 | 0.00020643 | 0.00020787 | 0.00031876 | 0.0037109 | 0.010514 | 0.023891 | 0.041331 | 0.043175 | 0.049191 | 0.047476 | 0.047408 | 0.054781 | 0.052998 | 0.051625 | 0.058623 | 0.056394 | 0.056296 | 0.053516 | 0.048648 | 0.048691 | 0.046311 | 0.046285 | 0.043508 | 0.041794 | 0.034454 | 0.022758 | 0.015885