## Slide 1: Hemispherical Confocal Imaging using Turtleback Reflector
Yasuhiro Mukaigawa (Osaka University)
Seiichi Tagawa (Osaka University)
Jaewon Kim (MIT Media Lab)
Ramesh Raskar (MIT Media Lab)
Yasuyuki Matsushita (Microsoft Research Asia)
Yasushi Yagi (Osaka University)
ACCV2010

## Slide 2: Motivation
Clear view of a particular depth in the scene
Reduction of undesirable phenomena such as
[Vaish et al. CVPR2004]
[Fuchs et al. EGSR2008]
Occlusion
Scattering

## Slide 3: Related works
Normal view
Synthetic aperture
Confocal imaging
Synthetic aperture confocal imaging
detector
source
Problems:
Limited aperture size
Scattering
[Levoy et al. SIGGRAPH2004]

## Slide 4: Our idea: Hemispherical confocal imaging
Specially designed polyhedral mirror
Synthesis of huge aperture
Pattern projection from many projectors
Focused illumination & descattering
Optical device
Image analysis

## Slide 5: Huge aperture
Advantages of huge aperture
  extremely shallow DOF
  clear view of the particular depth
DOF
Aperture
size
Small
Large
Huge
F-number: 0
FOV: 180 [degree]
Hemispherical aperture
does not exist
how to realize?
?

## Slide 6: Hemispherical synthetic aperture
Real camera
Synthetic aperture technique
  many cameras on a hemisphere
  uniform distance and density
  problems: cost and physical conflict
Virtual cameras using planar mirrors
Target object
Virtual cameras
Planar mirrors

## Slide 7: Design of polyhedral mirror
Real camera
Hemisphere
Target object
Geodesic dome
Ellipsoid
Virtual cameras
Projection onto
the ellipsoid

## Slide 8: Turtleback reflector
Simulation by POV-Ray
View from a real camera

## Slide 9: How to make turtleback reflector
Grind
Cut
First-surface mirror
Planar mirrors
Plastic frame
Turtleback reflector
(cost: 50US$)

## Slide 10: Overview of the imaging system
Projector
Camera
Turtleback reflector
Beam splitter

## Slide 11: Preliminary experiment (1)
Hemispherical synthetic aperture
# of camera
1
3
12
48
Small
Large
Hemisphere
Aperture
2mm
Textured paper
Orange mesh

## Slide 12: Preliminary experiment (2)
Covered by yellow dense mesh
Small
Large
Hemisphere
...
2400x2000

## Slide 13: Decomposition
Undesired phenomena
  reflection from unfocused depth
  scattering
Eliminate undesired components
Blurred mesh
Focused
depth
Light
source
Scattering
Reflection from
unfocused depth
Direct reflection from
the focused depth
Eliminate
Special illumination using
Turtleback reflector

## Slide 14: Special illumination
Focused illumination
High frequency illumination
Illuminate the particular depth
Separate direct / global components
New idea: Focused High Frequency Illumination (FHFI)
[Levoy et al. 2004]
[Nayar et al. 2006]
High frequency patterns are focused only on the particular depth

## Slide 15: Focused High Frequency Illumination
Projection of high frequency positive and negative patterns
  blurred in unfocused region
  constant scattering
Positive pattern
Negative pattern
Max – Min
Focused
Unfocused
Scattering
Positive
1
1/2
1/2
Negative
0
1/2
1/2
Max-Mix
1
0
0
Eliminated

## Slide 16: Experimental results of FHFI
Covered by orange mesh
Covered by diffuse sheet
Normal
illumination
FHFI
FHFI
+
Hemispherical aperture
Normal
illumination
FHFI
(descattering)
Hemispherical
aperture

## Slide 17: Position of our method
Synthetic aperture
Confocal imaging
Synthetic aperture confocal imaging
Confocal imaging with descattering
Hemispherical confocal imaging
bright
darken
unilluminated
darken
unilluminated
unnecessary
necessary
unnecessary
necessary
unnecessary
remaining
remaining
partially reduced
reduced
reduced
unfocused
depth
scanning
scattering
Limitations
  The resolutions of virtual cameras and projectors are low.
  The observable area is narrow.

## Slide 18: Conclusion
Hemispherical confocal imaging to see a clear view of the particular depth
  Hemispherical synthetic aperture by designing Turtleback reflector
  Clear view of the particular depth by FHFI
Future works: evaluation, application
(1)
(2)
(3)
Factorization (skipped)

## Slide 19
END

## Slide 20: Factorization
absorption
occlusion
A
B
C
x
x
=
Camera A
Camera B
Camera C
Dark regions due to absorption and occlusion
Factorization into three terms
Observed views
Masking terms
Reducing terms
Texture term

## Slide 21: Experimental result of Factorization
FHFI +
Hemispherical aperture
Observed views
Masking terms
Reducing terms
Texture term
...
x
=
x
...
...
Observed views from virtual cameras

## Slide 22: Factorization
observation
=
masking
X
attenuation
X
texture

## Slide 23: Design of Turtleback reflector
Virtual cameras and projectors on the nodes of a geodesic dome
Circumscribed polyhedron to ellipsoid
75mm
90mm
100mm

## Slide 24: Turtleback reflector
50 first-surface mirrors
Plastic base by Stereolithography

## Slide 25: Captured image
2mm
A
B
C
D
printed paper
transparent sheet
2000x1600